COBRETTIVIPERV8.COM

Updated Sunday, 23 April 2006

Chevy Small Block, Block Assembly

ITEM				NOTES				NUMBER

Block (bare)								1

Pistons & Pins			to suit bores				8

Rings, top			to suit bores				8

Rings second			to suit bores				8

Rings oil control		to suit bores				8 sets

Connecting rods							8

Connecting rod bolts		to suit rods				16

& nuts

Connecting rod		to suit crankshaft			8 pairs

Bearings

Front main bearing cap						1

No 2 main bearing cap						1

No 3 main bearing cap						1

No 4 main bearing cap						1

Rear main bearing cap						1

Main bearing bolts for		7/16” – 14 UNC x 3”			10

Pre 1968 small journal

cranks

Main bearing bolts for		7/16” 14 UNC X 3-1/4”		10

1968 and later large

Journal cranks

Main bearing bolts for		7/16” – 14 UNC x 3-3/8”		10

Four bolt mains long

Main bearing bolts for		7/16” – 14 UNC x 2”			6

Four bolt mains short

Water jacket freeze plugs	1-5/8” dia (cup)			8

(400CID four bolt main bearing engine requires 10 water jacket freeze plugs)

Cam bearing plug		2-3/32” dia (shallow cup)		1

Oil gallery plugs		1/2” dia (cup)				3

Oil gallery screw plugs	1/4” pipe thread x 7/16” long		3

Socket drive

Crankshaft								1

Crankshaft main 		to suit crankshaft			5 pairs

Bearings

Crankshaft vibration							1

Damper (harmonic balancer)

Crankshaft keys							2

Crankshaft pilot bushing	to suit crankshaft			1

(manual transmissions only)

Front pulley			with grooves to suit application	1

Front pulley bolts		3/8” – 24 UNF or			3

3/8” – 16 UNC x 1” long

(check damper for thread type)

Crankshaft vibration		7/16” – 20 UNF x 2-1/4” long	1

damper bolt

Crankshaft vibration							1

Damper bolt washer

Camshaft followers							16

(lifters or tappets)

Camshaft								1

ITEM				NOTES				NUMBER

Camshaft sprocket							1

Camshaft sprocket bolts	5/16” – 18 UNC x 1” long		3

Camshaft drive chain							1

Crankshaft gear							1

Crankshaft rear oil seal						1 pair

Cylinder head locating	5/16” dia x 1/2” long			4

Dowels

Dipstick tube								1

Dipstick								1

Flex plate								1

(auto transmission only)

Flywheel								1

(manual transmission only)

Flex plate or flywheel bolts	7/16” – 20 UNF length to suit		6

(must use correct grade from GM dealer or US spares supplier)

Oil pump								1

Oil pump securing bolt	7/16” – 14 UNC x 2-3/8” long	1

Oil pump pick up pipe							1

Oil pump drive shaft							1

Oil pump drive shaft adaptor						1

Oil pan				to suit chassis				1

Oil pan bolts (small)		1/4” – 20 UNC x 1/2” long		14

Oil pan bolt star washers	1/4” dia				14

Oil pan bolts (large)		5/16” – 18 UNC x 5/8” long		4

ITEM				NOTES				NUMBER

Front cover with oil seal						1

Front cover bolts		1/4” – 20 UNC x 1/2” long 		10

Front cover bolt star washers	1/4” dia				10

Front cover ignition timing						1

tag (if applicable)

Oil filter pressure relief	to suit filter				1

valve housing

Oil filter pressure relief	5/16” – 18 UNC x 1” long or		2

valve housing bolts		1/4” 0 20 UNC x 1-1/2” long

(check block)

Oil filter case or spin		check pressure relief valve housing	1

On cartridge

Oil filter securing bolt 	1/2” – 13 UNC x 9” for short  	1

For cartridge type filter	canister or 12” for long canister

(if applicable)

Water pump			extended or short to suit application	1

Water pump bolts for		3/8” – 16 UNC x 2” long		4

Extended pump

Water pump bolts for		3/8” – 16 UNC x 2-1/2” long and	1

Short pump			3/8” – 16 UNC x 1-5/8” long

Fuel pump pushrod							1

Fuel pump spacer plate						1

Fuel pump spacer plate bolts	1/4” – 20 UNC x 5/8” long		2

Oil pressure switch							1

Fuel pump								1

Fuel pump bolts		3/8” – 16 UNC x 1-1/4” long		2

The data herein has been verified as far as possible. We disclaim any liability incurred in connection with the use of this Data or any specific details mentioned herein.